## Slide 1: APRS Local and Global
RF and Around the World

## Slide 2: Automatic Position Reporting System
Original Name – Automatic Packet Reporting System
Developed in 1990 based on 2 meter AX.25
Designed for one-to-many communication of automated information
Support for SMS-like messaging (Short Messaging Service)

## Slide 3: One-to-Many Communication

## Slide 4: One-to-Many Communication
Not Broadcast (according to FCC).
Everyone sees all packets from everyone else.
Information of value to amateur radio communicated.
Two-way communication possible.
Unnumbered Information (UI) subset of AX.25
SHARED frequency.

## Slide 5: Examples of Local RF Uses
Track Resources
Quick Messaging
Locate Points of Interest
Special Events – Tracking and Communication

## Slide 6: Deprecated Local Uses
How far can a packet go? (Minimize hops)
How smooth a line can I paint? (Shared frequency, applies to APRS-IS-only devices such as smart phones)
“Tactical” callsigns outside of a special event (Use callsigns to enable global communications).
Objects for obvious locations - DFW Airport not ok, Collin County EOC ok.
Bulletins for recurring events (Use objects instead).

## Slide 7: IGate – Gateway to the World
APRS-IS – Interconnect Amateur Radio APRS RF networks
Worldwide messaging
Worldwide visibility
Requires unique station identification

## Slide 8: APRS-IS Architecture
Notes: Note the dual, unidirectional connections between servers.

## Slide 9: APRS-IS Today
9 core servers
88 aprs2.net servers
2680 IGates (incl. receive-only, not recommended)
1770 DGates (D-PRS IGates)
31,100 RF stations
18,700 Internet “stations”

## Slide 10: Bidirectional Coordination
IGates are like wide area, linked repeaters, on the same frequency
IGates receive packets from the Internet within milliseconds
Multiple bidirectional IGates in one area collide causing complete loss of gated packets
Excessive paths cause further loss of packets
Established 24/7 IGate should be considered higher priority than new IGate or less than 24/7 IGate

## Slide 11: APRS-IS Services
EMAIL-2 – Bidirectional Email
WHO-IS – QRZ.com Lookup
CQSRVR – CQ to like-minded hams
ANSRVR – Announcement server
NWS Warnings – Injected by AE5PL-WX

## Slide 12: I Want to Participate
Viewing
  http://aprs.fi (Well used map server)
  http://www.findu.com (Oldest database server)
  http://www.jfindu.net (javAPRS live mapping)

## Slide 13: I Want to Participate
http://www.aprs-is.net
GET ON RF
  Never beacon faster than 1 per minute
  Mobiles/portables – 3+ minute (WIDE1-1,WIDE2-1)
  Weather – 5 to 15 minutes (WIDE2-1)
  Repeater Objects – 10 minutes (WIDE2-1)
  Other Fixed – 20 minutes (WIDE2-1)

## Slide 14: Where do I Connect To?
It depends…
  Client or IGate with filtered feed (most common)
    Any core server, port 14580
    Any javAPRSSrvr or aprsc tier 2 server, port 14580
  Server providing full feed
    Any core server, port 10152
Check server status page (http://server.ip:14501) for regional ports

## Slide 15: What’s FireNet?
Originally a “subnet” of APRS-IS providing fire sighting information
Now supports METAR, buoy, earthquake, river, and ship information
As well as the entire APRS-IS feed
Filtered ports are available
http://firenet.us:14501

## Slide 16: Summary
APRS-IS is a high speed backbone interconnecting the local RF APRS networks world-wide.
Global messaging without routing.
Window for non-amateurs and RF challenged amateurs to participate in APRS.
Used by government agencies for emergency preparedness (NWS, for instance).
Mechanism for dissemination of relevant amateur related information world-wide.
Notes: Because of this giant backbone, ALL callsign-SSID combinations MUST be unique.

## Slide 17: Q&A
http://www.aprs-is.net
Peter Loveall AE5PL – pete@ae5pl.net